## Slide 1
to run ARM_CORE_EDP:
extract the ARM_CORE_EDP archive
Open matlab and go to the extracted directory
Run the command: ARM_CORE_EDP
extracted directory
matlab command

## Slide 2
If the code ran successfully, this GUI will pop up

## Slide 3
This is the physical design of the ARM chip, including:
- Inverters & buffers to meet timing constraints,
- Combinational logic to implement arithmetic in the core,
- And sequential logic to keep state for executing programs

## Slide 4
This is the physical design of the ARM chip, including:
- Inverters & buffers to meet timing constraints,
- Combinational logic to implement arithmetic in the core,
- And sequential logic to keep state for executing programs
You can toggle what is displayed. This is only for visualization (you don’t
need to do anything with this window)

## Slide 5
This is the main energy & delay for the ARM core

## Slide 6
Update the FET values with your values from Sentaurus

## Slide 7
The ARM core energy & frequency will be shown here

## Slide 8
For example, one way to increase clock frequency is by increasing VDD to increase on-current; here, VDD is increased to 2.2 V, and on-current is increased to 900 uA/um

## Slide 9
Then click “Analyze & Plot”

## Slide 10
And the new point is updated
Your most recent design
Is always shown in red

## Slide 11
Continuing to increase VDD & on-current
Increases both clock frequency & energy,
Which gives a trade-off for EDP

## Slide 12
And again… notice the EDP is getting worse (higher)

## Slide 13
In this case, the best EDP is in the middle of the curve

## Slide 14
You can also click “Clear Plot”
to remove all existing data from the plot

## Slide 15
Another strategy is the increase the threshold voltage, which lowers off-current at the cost of lower on-current

## Slide 16
As you will see, these parameters can be inherently difficult to trade-off! But remember – the specifications you want might not be the specifications you can achieve with your transistor! (extracted from Sentaurus)